## Slide 1
Austria´s DRS and its influence on the design and costs of packaging collection service
Andreas Pertl
Managing Director Austrian Packaging Coordination Office

## Slide 2: Packaging Coordination Office
The WMA offers the opportunity to responsible Ministry to establish a company which supports the Ministry to supervise and coordinate different activities in the competitive producer responsibility scheme.
  The Packaging Coordination Office (VKS) was established as a non-profit organisation by decision of the Ministry in 2014.
The VKS is owned by the Austrian Environmental Agency (Umweltbundesamt) which itself is owned by the Federal Republic of Austria = VKS is 100% state owned
All PROs have to contract with the VKS as obligatory requirement to get approved by the Ministry.
  Currently six producer responsibility organisations (PRO) are approved in Austria

## Slide 3: Legal framework
Waste Management Act
  Basic rules for the EPR and DRS scheme
  Rules for PROs and the VKS
Packaging Ordinance
  Collection and Recycling quota, restrictions for substances
  Roles for obligated companies and consumers
  Requirements for packaging and packaging waste prevention
Deposit Ordinance for Single-use Beverage Packaging
  Types of packaging and materials
  Registration of obligated companies and products
  Organization of the DRS – material and financial flows
  Tasks of the central agency (EWP Recycling Pfand Österreich gGmbH)
  Labelling and deposit amount = EUR 0,25

## Slide 4: Austria´s Deposit Return Scheme - Implementation
Legal steps…
  December 10th, 2021 – Amendment of the Waste Management Act
    Basic rules and possibility for an DRS on single-use beverage packaging from plastics and metals
  September 25th, 2023 – Deposit ordinance
  July 17th, 2024 – Amendment of the Waste Management Act
    Concretization of the set-up of the central agency (obligations, supervision, legal form,…)
Implementation
  March 2022 – Establishment of the supporting association by retailers and manufacturer
  December 2022 - Establishment of the central agency
  May 2023 – Concretization of the central agency (EWP Recycling Pfand Austria gGmbH)
  January 1st, 2025 – Operational start of the DRS in Austria (with a transition period)
    April 1st, 2025 – Ending of the possibility to fill obliged beverages without deposit
    December 31st, 2025 – Ending of the possibility to sell obliged beverages without deposit

## Slide 5: Austria´s Deposit Return Scheme - Operation
Affected packaging and products
  Single-use beverages from plastics (mostly PET bottles) and metals (mostly aluminium cans)
  Filling volume from 0,1 to 3,0 litres for all beverages except milk and dairy products
  Deposit = EUR 0,25
Involved actors
  Deposit collection = First distributor from their respective customer
  Take back and deposit payout = Final distributor (retail, bakeries, …) from and to customers
    Mostly by vending machines at retailers
    Manual collection for small amounts in special bags – counting stations operated by EWP
  Central agency = Organizes financial and material flows recycling and operates the registry
    Right of first refusal for recyclates for manufacturers from EWP
    Fees for producers = Costs - Revenues - Deposit slip
GOALS:
  Collection rates: 80% in 2025, 90% in 2027
  Ensure secondary resources to fulfil the minimum recycled content (25% in 2025, 30% in 2030)
Notes: (manufacturers, retail for their own brands, online trader)

## Slide 6: Impact of DRS on packaging EPR in Austria – Competition
market share
Consulting for obligated companies (recyclability, optimization of waste management systems, …)
Easier licencing for obligated companies
Overhead and internal efficiency
NO COMPETITION:
Collection service = shared use model
Sharing of costs
Sharing of collected wastes
Contracting with sorters, recyclers
Logistical performance
Sale of secondary resources
Obligated companies
PRO1
PRO1
PRO1
COLLECTION
Sorting
Sorting
Recycling
Recycling
FULL COST MODEL

## Slide 7: Impact of DRS on packaging EPR in Austria – Collection of household packaging
Collection by kerbside collection (rural areas) or collection points (urban and touristic areas) and municipal waste collection centers
Responsibilities for the organisation of collection:
  Lightweight, metals, glass: PROs (one specific PRO per “collection region”)
  Paper: Municipalities (as part of the paper waste collection)
Collection quota for household packaging by separate collection:
 | from 2023 | from 2025 | from 2030
Paper, cardboard | 80% | 80% | 85%
Glass | 80% | 80% | 85%
Metals | 60% |  | 
Ferrous metals |  | 65% | 75%
Aluminium |  | 65% | 75%
Plastics | 75% | 80% | 85%
Beverage cartons | 60% | 80% | 80%

## Slide 8: Impact of DRS on packaging EPR in Austria – Collection of household packaging
Loss of around 21-23% of material (mostly PET and aluminium) brought on the market and collected
January 1st, 2025: Mixed collection of lightweight & metal packaging in entire Austria
  Mostly in the Yellow Bag or Yellow Bin
  “Emergency” collection at waste collection centers
Adaption due to DRS started from two different forms of collections:
  Lightweight packaging only before 2025:
    Lost volume form PET bottles filled up with metal packaging
    No changes in collection frequency needed
  Existing mixed collection before 2025:
    Collection frequency stays the same during the transformation year 2025
    Evaluation of the collection frequency and reduction where useful beginning with 2026

## Slide 9: Impact of DRS on packaging EPR in Austria – Waste collection and costs
Evaluation on waste amounts and costs is still ongoing
  Reliable results in the beginning of 2026
General issues on costs:
  Higher tariffs for plastic and metal packaging in the EPR scheme
    Higher specific collection costs during the transition phase
    Lower revenues as highly valuable materials are in the DRS
    Higher sorting and recycling efforts to reach the 50% recycling rate in 2025
  Higher overall costs by dual collection scheme “DRS & EPR”.. BUT
    DRS is necessary to guarantee the fulfilment of the 90% collection quota goal
    Cost comparison with an existing EPR system with 90% collection rate is not possible
    Indirect cost reductions due to awaited lowered clean up costs of littered waste for municipalities

## Slide 10: Key reflections
Ambitious goals need ambitious budgets
Clear rules for the transition from EPR to DRS – by law or decision if necessary
  Fair allocation of costs forced by the transition process between EPR and DRS
  Cooperation between EPR and DRS should be initiated
Adoption of the lightweight packaging collection is necessary for cost efficiency
People are adopting very quickly from EPR to DRS
Grumbling (by affected companies, people and media) at the beginning is normal – regardless of changing separate collection or implementing a DRS
  Public relations and cooperation with municipalities is key to success!
The dual scheme of DRS and EPR is Austrias plan to reach the EU goals!
  Evaluation and optimization based on first experiences has started

## Slide 11: Thank you for your attention!
Dipl.-Ing. Andreas Pertl
Managing Director
T: +43 1 996 96 68-0
andreas.pertl@vks-gmbh.at
VKS Verpackungskoordinierungsstelle
gemeinnützige Gesellschaft mbH
Zieglergasse 8 / TOP 3, 1070 Vienna
http://www.vks-gmbh.at